## Slide 1: Extreme weather in project The West Link Johan Jansson 2015-05-28
Notes: Johan Jansson, mainly storm water and high water level issues in investment projects
Will bild a new railway tunnel in Gothenburg
Planning how to handle the extreme weather events

## Slide 2: Project “The West Link”
8 km (5 miles) new railway
6 km (4 miles) in tunnel
Three new stations
Construction 2017/2018
Traffic 2026
Notes: Looks like in one of the new railwaystations.
Access
Water is very close
Start in 2-3 years

## Slide 3
Notes: Lots of engineering has been done and will be
To get a nice, safe and dry railway
Below is one the station entrances – nobode wants the high levels into the tunnel

## Slide 4
Notes: Global perspective
Slides from the time for the descisions

## Slide 5
Sea water levels in Stockholm in years 1774-2012
Annual average water level [cm]
Year
Notes: In Stockholm meassurements for 250 years
Something happens in the last 50 years.
Isostatic uplift of the land

## Slide 6: Water level
Uplift
Global water level
Water level [cm]
Notes: Isostatic uplift
Break even in ten years

## Slide 7: Levels at station Haga
Chart: 
| 2000 | Byggnation 2018 - 2028 | 2100 | 2150
Havsnivåhöjning | 0 | 0 | 1 | 2
Variationer i dagens klimat | 2 | 2 | 2
Generell osäkerhetsnivå | 0.5 | 0.5 | 0.5
Högt scenario | 0.5 | 1
The West Link level ( m )
Protection level
Water level for train service
Protection level
Prepared higher level
Construction
2018-2028
High scenario
Uncertainty
Todays extreme events
Future rise in sea level
Notes: Construction
Protection
Train service
Is designed to be prepared to additional
If course been lots of discussion and descision making about protection levels
What do we want to protect
For how long time can it be not in use
How to protect..

## Slide 8
Teckenförklaring
Flooded areas

## Slide 9
Rain event 150 mm på 2 timmar in centre of Gothenburg
Water levels from short rain
Nedfart

## Slide 10
Water finds its way
Nedfart
Rain event 150 mm på 2 timmar in centre of Gothenburg

## Slide 11: High sea level + rain?
Not at the same time
Rainfall [mm/h]
Sea level [m]
Notes: If it happens at the same time? It doesn´t.
Sea level up
Rainfall to the right
There is no dots in the corner
but!

## Slide 12
Station Korsvägen: +4.9 m
Olskroken: +4.3 m
Station Haga: +4.0 m
Göta Älv: +4.0 m
Almedal: +5.1 m
Risks from high flows in river Mölndalsån and high sea level
Station Centralen: +4.3 m
Höjder i RH2000

## Slide 13
Gothenburg is looking forward
Year 2026
Year 2100
Notes: In the year 2026 nice, clean and dry tunnel
In the year 2100 its still dry