## Slide 1: Flood control, risk reduction and preparedness 10 years after Katrina
John H Pardue Louisiana State University

## Slide 2
Conducted early environmental sampling of Katrina floodwaters/sediments
Air sampling adjacent to debris piles
Analysis of debris handling procedures and techniques
Analysis and prediction of bulk chemical storage problems during flooding events

## Slide 3: Where are we?
Flood control and surge attenuation
  Structural elements (Greater New Orleans Hurricane and Storm Damage Risk Reduction System)
  Non-structural elements (Louisiana Coastal Master Plan 2012)
Environmental Risk
  Debris removal, landfills and contaminated soil

## Slide 4
Total cost: 14.6 billion

## Slide 6
IHNC Surge Barrier

## Slide 7: The criteria for commencing IHNC gate closure operations are:
Water elevations of 3 ft or greater in Lake Borgne
A storm is predicted to make landfall in the ‘area’ within three days
The general procedure is as follows:
  Closure of the Seabrook Gate by USACE, approximately 20 min;
  Closure of the Bayou Bienvenue Gate by USACE, approximately 20 min
  Closure of the GIWW Sector Gate by USACE, approximately 2 hours for sector gate and 7 hours for barge gate.
  Closure of the IHNC Navigation Lock by USACE.
Storm occurs
  GIWW Sector gate opened first (when maximum water elevation differential is ~3 ft) by USACE, approximately 2 hrs.
  Bayou Bienvenue Gate is opened by USACE, approximately 2 hrs.
  Once Lake Pontchartrain has drained, Seabrook Gate opened by USACEG, approximately 2 hrs.

## Slide 9
Total cost: 14.6 billion

## Slide 10
7,600 cfs
17th Street Canal Interim Closure Structure

## Slide 13: How do you build a system in 5 years?
NEPA (allowed USACE to to break up comprehensive Environmental Impact Statements (EISs) into smaller units of assessment)
Contracts (Design-build; early contractor involvement)
Non-traditional techniques (deep soil mixing, wick drains)

## Slide 14: NEPA
National Environmental Policy Act
  Establishes environmental review processes that apply to governmental actions
  Seek reasonable alternatives to actions that harm the environment
  An Environmental Impact Statement is prepared, public comment and review, followed by review by the Environmental Protection Agency
  Very long process

## Slide 15: NEPA (alternative arrangement)
In an emergency, an alternative arrangement is possible for compliance with NEPA
  Implemented in consultation with the Council on Environmental Quality, state and federal resource agencies
  Breaks impact studies up into smaller pieces directed at each individual action
  Still substantial alternatives discussed and mitigation efforts, still a significant public comment period

## Slide 18: Coastal Land Loss
Over 2300 square miles lost since 1930
Notes: 18
18
18

## Slide 19
DeWitt Braud, LSU Coastal Studies Institute
Landsat TM 1998
Terrebonne Land/Water Change 1988-2005
Dulac
Chauvin
Cocodrie
Point Barre
Lafourche
Notes: 19
Cocodrie is in the lower left corner of the image.

## Slide 22
50 million dollar—estimated costs of all projects

## Slide 23
Caminada Headland Beach (Fourchon Beach and Elmer’s Island)

## Slide 24
5.1 milliion cubic yards for the beach/dune
5,36 million cubic yards for the marsh

## Slide 32: Data and knowledge gaps
How do structural and non-structural flood control/surge attenuation work together as a system to minimize damage?
How do non-structural elements of the system mitigate surge?
How resilient are the non-structural elements after storm impacts?

## Slide 33: Depth-dependent roughness
Cypress-tupelo and bottomland hardwood forest dominated by vegetation that is on the scale of relevant surges, marshes by vegetation much shorter than relevant storm surges

## Slide 34
Chris Granger, The Times-Picayune archive
> 100 million cubic yards of debris

## Slide 35
Debris Handling System
Housing contents to curbside by resident
Environmental and disposal teams circulate through neighborhoods and remove visible wastes targeted for segregation
Staging area followed by proper disposal
[14.3 M lbs HHW
794,891 White goods
5 M orphan containers
940,000 e-waste]
Remaining debris to C&D landfill
Inspection at tower and by spotters assigned to landfill face
Disposal

## Slide 36: Analysis and critique of Katrina debris-handling system
No diversion of arsenic-treated lumber
  Potential impacts: arsenic contamination of groundwater
  LWRRI White Paper “Anticipating environmental problems in landfills in New Orleans East ”
  Quantities of Arsenic-Treated Wood in Demolition Debris Generated by Hurricane Katrina; B. Dubey, H. M. Solo-Gabriele, and Timothy G. Townsend; Environ. Sci. Technol.; 2007; 41(5) pp 1533 – 1536
No diversion of wallboard
  Potential impacts: generation of H2S in landfill
  SWANA analysis of Katrina debris plan (2005)
  LWRRI White Paper

## Slide 37: Analysis and critique of Katrina debris handling system
Inefficient household hazardous waste diversion
  Potential impacts: contamination of groundwater by HHW
  LWRRI White Paper “Anticipating environmental problems in landfills in New Orleans East ”
  LSU pile sampling and air sampling
Utilization of C&D landfills for disposal
  Potential impacts: groundwater contamination
  NISTAC (FEMA) Draft Report, 2006
  Criticized by a very wide range of constituencies

## Slide 38
Old Gentilly Monitoring Well Data
Maximum metal concentrations:
As: 1.4 mg/L
Zn: 6,850 mg/L
Ni: 0.97 mg/L

## Slide 39: “Old Gentilly Landfill Not the Disaster Once Feared” 2012
Limited sampling for limited set of analytes
No air sampling for H2S (of primary concern due to deposition of very large volumes of gypsum wallboard)
Nearly zero information to inform future events (Joplin tornado using very similar debris handling methodology)

## Slide 40: Soil contamination issues continue
Lead, PAH contamination remain extremely common
Katrina dropped blood lead levels in children (Mielke, ES&T) presumably due to a fresh layer of soil covering
Very large soil removal action underway at B.F. Cooper housing development

## Slide 41: Questions??